## Slide 1: Ohm’s Law
Page 306 - 307

## Slide 2: Georg Simon Ohm
He experimented with many substances and proved a mathematical link between voltage (V), current (I) and resistance (R).
The unit of resistance Ohm was named in his honour.

## Slide 3: Ohm’s law states that…
As long as the temperature stays the same:
  The resistance of a conductor stays constant
  The current is directly proportional to the voltage applied.
In other words, if the voltage increases, current also increases.

## Slide 4: Ohm’s Law
Quantity | Symbol | Unit | Calculated with Ohm’s Law | Measured with
Voltage | V | Volts (V) | V = I x R | Voltmeter
Current | I | Amps (A) | I = V/R | Ammeter
Resistance | R | Ohms (Ω) | R = V/I | ohmmeter
R
V
I

## Slide 5: Applying Ohm’s Law
If we know two of the values, we can solve for the third!
Example:
  An electric stove is connecter to a 240V outlet. If the current flowing through the stove is 20 A, what is the resistance of the heating element?
    Identify known quantities: current = 20A, voltage = 240V
    Identify the unknown quantity: resistance = ?
    Choose the right formula: R = V/I
    Solve: R = 240V/20A
    R = 12 Ω

## Slide 6: Example 2
A 30-V battery creates a current through a 15- Ω resistor. How much current is created?
    Identify known quantities: V = 30V R= 15 Ω
    Identify the unknown quantity: I = ?
    Choose the right formula: I = V/R
    Solve: I = 30V/15 Ω
    I = 2A

## Slide 7: Example 3
A motor has an internal resistance of 40Ω. The motor is in a circuit with a current of 4.0A. What is the voltage?
    Identify known quantities: R = 40 Ω I = 4.0A
    Identify the unknown quantity: V = ?
    Choose the right formula: V = IxR
    Solve: V = 40 Ω x 4.0A
  V = 160 V